## Slide 1: Light + Color + Image
Human Visual System

## Slide 2: Human Visual System
2
Aperture letting in light
Controls pupil
Lens…
Slide Credit: NIH

## Slide 3: What is the Retina made of?

## Slide 4: Rod / Cone Sensitivity

## Slide 5: Rod / Cone Distribution

## Slide 6: What is light?
Light is electromagnetic radiation

## Slide 7: Electromagnetic Spectrum

## Slide 8: The Physics of Light

## Slide 9: Color Perception in Human
Color is the visual sensation
Red
400 700
Yellow
400 700
Blue
400 700
Purple
400 700

## Slide 10: Color Perception

## Slide 11: "Do you see what I see?

## Slide 12: Color Vision in Animals
Birds have four types of cones: can see ultraviolet light
Some flowers have “Nectar Guides” visible under UV light
Visible Light
UV light
Human cones also sensitive to UV light! But blocked by lens

## Slide 13: Color Vision in Animals
Mantis Shrimp: Up to 16 types of photoreceptors!
Can also detect polarization of light!

## Slide 14: Digital Image

## Slide 15: What is a digital image?
An image is a visual representation of a scene.
In computer vision we usually operate on digital (discrete) images:
The image can now be represented as a matrix of integer values
Source: S. Seitz

## Slide 16: Images as functions
Notes: demo with scanalyze on laptop

## Slide 17: Images as functions
We can think of an image as a function, f, from R2 to R:
  f( x, y ) gives the intensity at position ( x, y )
  Realistically, we expect the image only to be defined over a rectangle, with a finite range:
    f: [a,b] x [c,d]  [0,1]
A color image is just three functions pasted together. We can write this as a “vector-valued” function:
Notes: As opposed to [0..255]

## Slide 18: Digital Images
Theoretically images are continuous 2D functions of reflected scene brightness.
  (i, j) or (column, row) or (x, y)
To process on a computer we need a discrete representation
  Sample
  Quantise
=
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 20 | 0 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 75 | 75 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 75 | 95 | 95 | 75 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 96 | 127 | 145 | 175 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 175 | 175 | 175 | 255 | 255 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 255 | 255 | 255
255 | 255 | 127 | 145 | 200 | 200 | 175 | 175 | 95 | 47 | 255 | 255
255 | 255 | 127 | 145 | 145 | 175 | 127 | 127 | 95 | 47 | 255 | 255
255 | 255 | 74 | 127 | 127 | 127 | 95 | 95 | 95 | 47 | 255 | 255
255 | 255 | 255 | 74 | 74 | 74 | 74 | 74 | 74 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255

## Slide 19: Digital Images – Sampling
Sample the continuous 2D function into discrete elements.
Sensor
  2D array
  Photosensitive elements
  Non photosensitive gaps
Issues
  Elements have a fixed area
  Gaps

## Slide 20: Digital Images – Sampling
How many samples do we need ?
  Wasted space and computation time
  Enough for the objects of interest

## Slide 21: Digital Images – Quantisation
Represent the individual image points as digital values.
  Typically 8 bits

## Slide 22: Colour Images
Luminance only
  Simple representation
  Humans can understand
Colour images ( luminance + chrominance )
  Multiple channels (typically 3)
  Around 16.8 million colours
  More complex to process
  Facilitate certain operations

## Slide 23: Digital camera
A digital camera replaces film with a sensor array
  Each cell in the array is light-sensitive diode that converts photons to electrons
  Two common types
    Charge Coupled Device (CCD)
    Complementary metal oxide semiconductor (CMOS)
  http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 24: CCD vs. CMOS
CCD: transports the charge across the chip and reads it at one corner of the array. An analog-to-digital converter (ADC) then turns each pixel's value into a digital value by measuring the amount of charge at each photosite and converting that measurement to binary form
CMOS: uses several transistors at each pixel to amplify and move the charge using more traditional wires.
http://www.dalsa.com/shared/content/pdfs/CCD_vs_CMOS_Litwiller_2005.pdf
http://electronics.howstuffworks.com/digital-camera.htm

## Slide 25: Issues with digital cameras
Noise
    low light is where you most notice noise
    light sensitivity (ISO) / noise tradeoff
    stuck pixels
Resolution: Are more megapixels better?
    requires higher quality lens
    noise issues
In-camera processing
    oversharpening can produce halos
RAW vs. compressed
    file size vs. quality tradeoff
Blooming
    charge overflowing into neighboring pixels
Color artifacts
    purple fringing from microlenses, artifacts from Bayer patterns
    white balance
More info online:
  http://electronics.howstuffworks.com/digital-camera.htm
  http://www.dpreview.com/
Slide by Steve Seitz

## Slide 26: Color sensing in camera: Color filter array
Source: Steve Seitz
Estimate missing components from neighboring values (demosaicing)
Why more green?
Bayer grid
Human Luminance Sensitivity Function

## Slide 27: Demosaicing Result

## Slide 28: Problem with demosaicing: color moire

## Slide 29: The cause of color moire
detector
Fine black and white detail in image
misinterpreted as color information

## Slide 30: Color sensing in camera: Prism
Requires three chips and precise alignment
More expensive
CCD(B)
CCD(G)
CCD(R)

## Slide 31: Color sensing in camera: Foveon X3
Source: M. Pollefeys
http://en.wikipedia.org/wiki/Foveon_X3_sensor
http://www.foveon.com/article.php?a=67
CMOS sensor
Takes advantage of the fact that red, blue and green light penetrate silicon to different depths
better image quality

## Slide 32: Colour Images – RGB Images
Red-Green-Blue images
  Most common
  Channels correspond roughly to
    Red (700nm)
    Green (546nm)
    Blue (436nm)
  Colours combined in display

## Slide 33: Colour Images – RGB Images
Converting to Greyscale
  Y = 0.299R + 0.587G + 0.114B

## Slide 34: Colour Images – CMY Images
Cyan-Magenta-Yellow images
  Secondary colours
  Subtractive colour scheme
    C = 255 – R
    M = 255 – G
    Y = 255 – B
  Often used in printers
CMY is not directly supported in OpenCV.

## Slide 35: Colour Images – YUV Images
Used for analogue television signals
  PAL, NTSC
  4 Y to 1 U to 1 V
Conversion from RGB
  Y = 0.299R + 0.587G + 0.114B
  U = 0.492 * (B-Y)
  V = 0.877 * (R-Y)

## Slide 36: Colour Images – HLS Images
Hue-Luminance-Saturation images
  Separates Luminance & Chrominance
  Values we humans can relate to…
    Hue 0o..360o
    Luminance 0..1
    Saturation 0..1
  Watch out for circular Hue…

## Slide 37: Colour Images – HLS Images
Conversion from RGB
cvtColor(bgr_image, hls_image, CV_BGR2HLS);
// Hue ranges from 0 to 179.

## Slide 38: Colour Images – Other colour spaces
HSV
YCrCb
CIE XYZ
CIE L*u*v*
CIE L*a*b*
Bayer

## Slide 39: Colour Images – Skin detection
(S >= 0.2) AND
(0.5 < L/S <3.0) AND
(H <= 28o OR H >= 330o)
uchar H = hls_image.at<Vec3b>(row,col)[0];
uchar L = hls_image.at<Vec3b>(row,col)[1];
uchar S = hls_image.at<Vec3b>(row,col)[2];
double LS_ratio = ((double) L) / ((double) S);
bool skin_pixel = (S >= 50) && (LS_ratio > 0.5) &&
(LS_ratio < 3.0) && ((H <= 14) || (H >= 165));

## Slide 40: Colour Images – Red eye detection
(L >= 0.25) AND
(S >= 0.4) AND
(0.5 < L/S <1.5) AND
(H <= 14o OR H >= 324o)
uchar H = hls_image.at<Vec3b>(row,col)[0];
uchar L = hls_image.at<Vec3b>(row,col)[1];
uchar S = hls_image.at<Vec3b>(row,col)[2];
double LS_ratio = ((double) L) / ((double) S);
bool skin_pixel = (L >= 64) && (S >= 100) &&
(LS_ratio > 0.5) && (LS_ratio < 1.5) &&
((H <= 7) || (H >= 162));

## Slide 41: Noise
Affects most images
Degrades the image
Can cause problems with processing
Causes?
Measuring noise:
Correcting noise…
Types
  Gaussian
  Salt and Pepper

## Slide 42: Noise - Models
Additive noise
Multiplicative noise

## Slide 43: Noise – Salt and Pepper Noise
Impulse noise
Noise is maximum or minimum values

## Slide 44: Noise – Gaussian Noise
Good approximation to real noise
Distribution is Gaussian (mean & s.d.)

## Slide 45: Noise – Gaussian Noise Generation
Select value for σ
Determine distribution
For every pixel (x,y)
  f*(x,y) = g(x,y) + argmini(abs( rand() - Pcum[i] ))
  Set
    f(x,y) = 0 if f*(x,y) < 0
    f(x,y) = G-1 if f*(x,y) > G-1
    f(x,y) = f*(x,y) otherwise
Truncation attenuates Gaussian nature of noise

## Slide 46: LINEAR FILTERING

## Slide 47: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 48: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 49: Motivation: Noise reduction
Given a camera and a still scene, how can you reduce noise?
Take lots of images and average them!
What’s the next best thing?
Source: S. Seitz
Notes: Answer: take lots of images, average them

## Slide 50: Moving average
Let’s replace each pixel with a weighted average of its neighborhood
The weights are called the filter kernel
What are the weights for the average of a 3x3 neighborhood?

## Slide 51: Moving Average In 2D
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ones, divide by 9

## Slide 52: Moving Average In 2D
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ones, divide by 9

## Slide 53: Moving Average In 2D
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ones, divide by 9

## Slide 54: Moving Average In 2D
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ones, divide by 9

## Slide 55: Moving Average In 2D
 | 0 | 10 | 20 | 30 | 30 |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ones, divide by 9

## Slide 56: Moving Average In 2D
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 0 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 90 | 90 | 90 | 90 | 90 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 90 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 0 | 10 | 20 | 30 | 30 | 30 | 20 | 10 | 
 | 0 | 20 | 40 | 60 | 60 | 60 | 40 | 20 | 
 | 0 | 30 | 60 | 90 | 90 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 30 | 50 | 80 | 80 | 90 | 60 | 30 | 
 | 0 | 20 | 30 | 50 | 50 | 60 | 40 | 20 | 
 | 10 | 20 | 30 | 30 | 30 | 30 | 20 | 10 | 
 | 10 | 10 | 10 | 0 | 0 | 0 | 0 | 0 | 
Notes: ones, divide by 9

## Slide 57: Key properties Linear Filters
Linearity: filter(f1 + f2 ) = filter(f1) + filter(f2)
Shift invariance: same behavior regardless of pixel location: filter(shift(f)) = shift(filter(f))
Theoretical result: any linear shift-invariant operator can be represented as a convolution

## Slide 58: Defining Convolution
f
Let f be the image and g be the kernel. The output of convolving f with g is denoted f * g.
Convention: kernel is “flipped”
MATLAB: conv2 (also imfilter)

## Slide 59: Properties in more detail
Commutative: a * b = b * a
  Conceptually no difference between filter and signal
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = […, 0, 0, 1, 0, 0, …], a * e = a

## Slide 60: Annoying details
What is the size of the output?
MATLAB: conv2(f, g,shape)
  shape = ‘full’: output size is sum of sizes of f and g
  shape = ‘same’: output size is same as f
  shape = ‘valid’: output size is difference of sizes of f and g
f
g
g
g
g
f
g
g
g
g
f
g
g
g
g
full
same
valid

## Slide 61: shape = ‘valid’
90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0

## Slide 62: shape = ‘same’
90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0

## Slide 63: shape = ‘full’
90 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 20 | 10 | 40 | 0 | 0
0 | 10 | 20 | 30 | 0 | 20 | 10 | 0 | 0 | 0
0 | 10 | 0 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 10 | 40 | 30 | 20 | 10 | 0 | 0
0 | 10 | 20 | 30 | 30 | 20 | 10 | 0 | 0 | 0
0 | 0 | 10 | 20 | 20 | 0 | 10 | 0 | 20 | 0
0 | 0 | 0 | 10 | 10 | 10 | 0 | 0 | 0 | 0

## Slide 64: Annoying details
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods:
    clip filter (black)
    wrap around
    copy edge
    reflect across edge
Source: S. Marschner

## Slide 65: Annoying details
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods (MATLAB):
    clip filter (black): imfilter(f, g, 0)
    wrap around: imfilter(f, g, ‘circular’)
    copy edge: imfilter(f, g, ‘replicate’)
    reflect across edge: imfilter(f, g, ‘symmetric’)
Source: S. Marschner

## Slide 66: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 67: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 68: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 69: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 70: Practice with linear filters
Original
?
1
1
1
1
1
1
1
1
1
Source: D. Lowe

## Slide 71: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
Blur (with a
box filter)
Source: D. Lowe

## Slide 72: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 73: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average

## Slide 74: Sharpening
before
after

## Slide 75: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 76: Smoothing with box filter revisited
Smoothing with an average actually doesn’t compare at all well with a defocused lens
Most obvious difference is that a single point of light viewed in a defocused lens looks like a fuzzy blob; but the averaging process would give a little square
Source: D. Forsyth
Notes: I always walk through the argument on the left rather carefully; it gives some insight into the
significance of impulse responses or point spread functions.

## Slide 77: Smoothing with box filter revisited
Smoothing with an average actually doesn’t compare at all well with a defocused lens
Most obvious difference is that a single point of light viewed in a defocused lens looks like a fuzzy blob; but the averaging process would give a little square
Better idea: to eliminate edge effects, weight contribution of neighborhood pixels according to their closeness to the center, like so:
“fuzzy blob”
Source: D. Forsyth
Notes: I always walk through the argument on the left rather carefully; it gives some insight into the
significance of impulse responses or point spread functions.

## Slide 78: Gaussian Kernel
Constant factor at front makes volume sum to 1 (can be ignored, as we should re-normalize weights to sum to 1 in any case)
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Source: C. Rasmussen

## Slide 79: Choosing kernel width
Gaussian filters have infinite support, but discrete filters use finite kernels
Source: K. Grauman

## Slide 80: Choosing kernel width
Rule of thumb: set filter half-width to about 3 σ

## Slide 81: Example: Smoothing with a Gaussian

## Slide 82: Mean vs. Gaussian filtering

## Slide 83: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
Convolution with self is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width σ√2
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 84: Separability of the Gaussian filter
Source: D. Lowe

## Slide 85: Separability example
*
*
=
=
2D convolution (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform convolution along rows:
Followed by convolution along the remaining column:
For MN image, PQ filter: 2D takes MNPQ add/times, while 1D takes MN(P + Q)

## Slide 86: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 87: Alternative idea: Median filtering
A median filter operates over a window by selecting the median intensity in the window
Is median filtering linear?
Source: K. Grauman
Notes: Linearity of median filter: try filter([0 0 0; 0 1 0; 0 0 0] + [1 1 1; 1 1 2; 2 2 2])

## Slide 88: Median filter
Replace each pixel by the median over N pixels (5 pixels, for these examples). Generalizes to “rank order” filters.
5-pixel neighborhood
In:
Out:
In:
Out:
Spike noise is removed
Monotonic edges remain unchanged
Median([1 7 1 5 1]) = 1
Mean([1 7 1 5 1]) = 2.8

## Slide 89: Median filtering results
Best for salt and pepper noise

## Slide 90: Median vs. Gaussian filtering
3x3
5x5
7x7
Gaussian
Median

## Slide 91: Edges

## Slide 92: Edge detection
Goal: Identify sudden changes (discontinuities) in an image
  Intuitively, most semantic and shape information from the image can be encoded in the edges
  More compact than pixels
Ideal: artist’s line drawing (but artist is also using object-level knowledge)
Source: D. Lowe

## Slide 93: Origin of edges
Edges are caused by a variety of factors:
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity
Source: Steve Seitz

## Slide 94: Characterizing edges
An edge is a place of rapid change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative

## Slide 95: Intensity profile
Source: D. Hoiem

## Slide 96: Edges in the Visual Cortex
Extract compact, generic, representation of image that carries sufficient information for higher-level processing tasks
Essentially what area V1 does in our visual cortex.
http://www.usc.edu/programs/vpl/private/photos/research/retinal_circuits/figure_2.jpg

## Slide 97: Image gradient
The gradient points in the direction of most rapid increase in intensity
The gradient of an image:
The gradient direction is given by
Source: Steve Seitz
The edge strength is given by the gradient magnitude
How does this direction relate to the direction of the edge?
Notes: give definition of partial derivative: lim h->0 [f(x+h,y) – f(x,y)]/h

## Slide 98: Differentiation and convolution
Recall, for 2D function,
This is linear
Differentiation is linear
  Derivative of shifted signal is shifted derivative
Source: D. Forsyth, D. Lowe

## Slide 99: Differentiation and convolution
Hence, differentiation can be represented as convolution!
  We could approximate this as
  which is obviously a convolution
-1 | 1
Source: D. Forsyth, D. Lowe

## Slide 100: Images as Functions
Remember:
Image is function f(x,y)
Approximate:
Another one:
-1
1
-1
0
1

## Slide 101: Finite difference filters
Other approximations of derivative filters exist:
Why might people use these compared to [-1,0,1]?
101
 | Horizontal | Vertical
Prewitt |  | 
Sobel |  | 
 | Horizontal | Vertical
Prewitt |  | 
Sobel |  | 

## Slide 102: Finite differences: example
Which one is the gradient in the x-direction (resp. y-direction)?

## Slide 103: Effects of noise
Consider a single row or column of the image
  Plotting intensity as a function of position gives a signal
Where is the edge?
Source: S. Seitz
Notes: How to fix?

## Slide 104: Effects of noise
Finite difference filters respond strongly to noise
  Image noise results in pixels that look very different from their neighbors
  Generally, the larger the noise the stronger the response
What is to be done?
  Smoothing the image should help, by forcing pixels different from their neighbors (=noise pixels?) to look more like neighbors
Source: D. Forsyth

## Slide 105: Solution: smooth first
To find edges, look for peaks in
f
g
f * g
Source: S. Seitz

## Slide 106: Derivative theorem of convolution
Differentiation is convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 107: Derivative of Gaussian filter
Which one finds horizontal/vertical edges?
x-direction
y-direction

## Slide 108: Scale of Gaussian derivative filter
Smoothed derivative removes noise, but blurs edge. Also finds edges at different “scales”.
1 pixel
3 pixels
7 pixels
Source: D. Forsyth

## Slide 109: Implementation issues
The gradient magnitude is large along a thick “trail” or “ridge,” so how do we identify the actual edge points?
How do we link the edge points to form curves?
Source: D. Forsyth
Notes: Figures show gradient magnitude of zebra at two different scales

## Slide 110: Designing an edge detector
Criteria for an “optimal” edge detector:
  Good detection: the optimal detector must minimize the probability of false positives (detecting spurious edges caused by noise), as well as that of false negatives (missing real edges)
  Good localization: the edges detected must be as close as possible to the true edges
  Single response: the detector must return one point only for each true edge point; that is, minimize the number of local maxima around the true edge
Source: L. Fei-Fei

## Slide 111: Canny edge detector
This is probably the most widely used edge detector in computer vision
Theoretical model: step-edges corrupted by additive Gaussian noise
Canny has shown that the first derivative of the Gaussian closely approximates the operator that optimizes the product of signal-to-noise ratio and localization
MATLAB: edge(image, ‘canny’)
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Source: L. Fei-Fei

## Slide 112: Canny edge detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression:
  Thin multi-pixel wide “ridges” down to single pixel width
Source: D. Lowe, L. Fei-Fei

## Slide 113: Non-maximum suppression
At q, we have a maximum if the value is larger than those at both p and at r. Interpolate to get these values.
Source: D. Forsyth

## Slide 114: Example
original image (Lena)

## Slide 115: Example
norm of the gradient

## Slide 116: Example
thresholding

## Slide 117: Example
Non-maximum suppression

## Slide 118: Canny edge detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression
  Thin multi-pixel wide “ridges” down to single pixel width
Linking of edge points
Source: D. Lowe, L. Fei-Fei

## Slide 119: Edge linking
Assume the marked point is an edge point. Then we construct the tangent to the edge curve (which is normal to the gradient at that point) and use this to predict the next points (here either r or s).
Source: D. Forsyth

## Slide 120: Canny edge detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression
  Thin multi-pixel wide “ridges” down to single pixel width
Linking of edge points
  Hysteresis thresholding: use a higher threshold to start edge curves and a lower threshold to continue them
Source: D. Lowe, L. Fei-Fei

## Slide 121: Hysteresis thresholding
Use a high threshold to start edge curves and a low threshold to continue them
  Reduces drop-outs
Source: S. Seitz

## Slide 122: Hysteresis thresholding
original image
high threshold
(strong edges)
low threshold
(weak edges)
hysteresis threshold
Source: L. Fei-Fei

## Slide 123: Effect of  (Gaussian kernel spread/size)
Canny with
Canny with
original
The choice of  depends on desired behavior
  large  detects large scale edges
  small  detects fine features
Source: S. Seitz

## Slide 124: Edge detection is just the beginning…
Berkeley segmentation database: http://www.eecs.berkeley.edu/Research/Projects/CS/vision/grouping/segbench/
image
human segmentation
gradient magnitude